## Slide 1: Real-Time Mutli-core Scheduling
Moris Behnam

## Slide 2: Introduction
Single processor scheduling
  E.g., t1(P=10,C=5), t2(10, 6)
  U=0.5+0.6>1
  Use a faster processor
Thermal and power problems impose limits on the performance of single-core
Multiple processor (multicore)
Problem formulation
  Given a set of real time task running on Multicore architecture, find a scheduling algorithm that guarantee the scheduability of the task set.

## Slide 3: Task model
Periodic task model ti(T,C,D)
  Releases infinite jobs every P period
  For all ti if P=D, Implicit‐deadlines
  If P>D, Constrained deadline
  Otherwise, Arbitrary deadlines
Sporadic task model ti(P,C,D)
  P is the minimum inter arrival time between two consecutive jobs
A task is not allowed to be executed on more than one processor/core at the same time.
ti
ji1
ji2
ji3
Ti
Ti
Ti
  //Control task Tci
  t = CurrentTime;
  LOOP
  S=read_sensor();
  Statement1;
  .
  .
  Statement2;
  Actuate;
  t = t + Tci;
  WaitUntil(t);
  END
ti
ji1
ji2
Ti
Ti
  //Monitor task Mci
  t = CurrentTime;
  LOOP
  S=read_sensor();
  Statement1;
  .
  .
  Statement2;
  Actuate;
  WaitUntil(sensor_signal);
  END

## Slide 4: Task model
Task utilization ti , Ui=Ci/Ti
Task density δi= Ci/min(Ti, Di)
The processor demand bound function h(t) corresponds to the maximum amount of task execution that can be released in a time interval [0, t)
The processor load is the maximum value of the processor demand bound divided by the length of the time interval
A simple necessary condition for task set feasibility

## Slide 5: Multicore platefrom
Include several processors on a single chip
Different cores share either on- or off-chip caches
Cores are identical (homogenous)
L1 Cache
L1 Cache
L1 Cache
L1 Cache
L2 Cache
Processor
Core 1
Processor
Core 2
Processor
Core 3
Processor
Core 4

## Slide 6: Design space
Tasks allocation
  no migration
  task migration
  job migration
Priority
  fixed task priority
  fixed job priority
  dynamic priority
Scheduling constraints
  non-preemption
  fully preemption
  limited preemption
time
P1
P2
t1
t2
t3
t3
t1
t2
time
P1
P2
t1
t2
t3
t3
t1
t2
time
P1
P2
t1
t2
t3
t3
t1
t2
t2
time
t1
t2
time
t1
t2
t2
time
t1
t2
t1
t2

## Slide 7: Mutliprocessor scheduling
Partitioned scheduling
Global scheduling
P1
P2
P3
…
Tasks
Processors
P1
P2
P3
…
Tasks
Processors

## Slide 8: Partitioned scheduling
Advantages
  Isolation between cores
  No migration overhead
  Simple queus managements
  Uniprocessor scheduling and analysis
Disadvantage
  Task set allocation (NP hard problem)
  Bin packing heuristics
    First-Fit (FF)
    Next-Fit (NF)
    Best-Fit (BF)
    Worst-Fit (WF)
    Task orderings in Decreasing Utilisation (DU) combined with above
U=1
Ci/Ti

## Slide 9: Partitioned scheduling
The largest worst-case utilization bound for any partitioning algorithm is
  U=(m+1)/2
Implicit deadline task set
Utilization bounds for the RMST (“Small Tasks”)
RM-FFDU has a utilization bound
Utilization bound for any fixed task priority
For EDF-BF and EDF-FF with DU
m +1 tasks with execution time 1+ε and a period of 2, Ui>0.5,
cannot be scheduled on m processors independent on
the scheduling and allocation algorithms.

## Slide 10: Partitioned scheduling
Constrained and arbitrary dealine
FFB-FFD algorithm (deadline monotonic with decreasing density) and assuming
  constrained-deadlines
  arbitrary deadlines
EDF-FFD (decreasing density)
  constrained-deadlines
  arbitrary deadlines

## Slide 11: Global scheduling
Advantages
  Fewer context switches / pre-emptions
  Unused capacity can be used by all other tasks
  More appropriate for open systems
Disadvantages
  Job migration overhead

## Slide 12: Global scheduling
Implicit deadline and periodic tasks
Global RM, fully preemptive and migration
example: n=m+1, t1,..,tn-1(C=2ε, T=1), tn(C=1, T=1 + ε)
Increase the priority of tn
time
P1
Pm
t1
tn
tm
t1
tm
Miss deadline
Utilization bound ≈0
time
P1
Pm
t1
tn
tm
t1
tm

## Slide 13: Global scheduling
RM‐US(m/(3m‐2) algorithm
Tasks are categorized based on their utilization
A task ti is considered heavy if Ci/Ti > m/(3m‐2)
Otherwise it is considered as light
Heavy tasks assigned higher priority than lighter
RM is applied on the light tasks to assign priority
Utilization bound is URM‐US(m/(3m‐2)=m*m/(3m‐2)
Example: suppose a systems has n=4, m=3 with the following task parameters t1 (0.4,4), t2 (0.6,6), t3 (0.45,9), t4 (8,10), then the priority assignment according to the algorithm will be, the highest for t4 as it is a heavy task and then t1, t2, t3 (lowest), based on RM.

## Slide 14: Global scheduling
Global EDF, fully preemptive and migration (fixed job priority, dynamic task priority)
Utilization based, UEDF = m − (m −1)umax
Same problem as in global RM
time
P1
Pm
t1
tn
tm
t1
tm
Miss deadline
time
P1
Pm
t1
tn
tm
t1
tm

## Slide 15: Global scheduling
EDF‐US(m/(2m‐1) algorithm
Tasks are categorized based on their utilization
A task ti is considered heavy if Ci/Ti > m/(2m‐1)
Otherwise it is considered as light
Heavy tasks assigned higher priority than lighter
Relative priority order based on EDF is applied on the light tasks
Utilization bound is UEDF‐US(m/(2m‐1)=m*m/(2m‐1)

## Slide 16: Global scheduling
Constrained and arbitrary deadline
Critical instant
  In uniprocessor, when all tasks are released simultaneously
  In multiprocessor it is not the case as shown in the following example
  Example: suppose a system with n=4, m=2, t1 (C=2,D=2,T=8), t2 (2,2,10), t3 (4,6,8), t4 (4,7,8)
Deadline miss

## Slide 17: Global scheduling
Determining the schedulability of sporadic task sets
  Consider an interval from the release to the deadline of some job of task tk
  Establish a condition necessary for the job to miss its deadline, for example each processor executes other tasks more than Dk −Ck
  Derive an upper bound IUB on the maximum interference in the interval from jobs released in the interval and also from jobs that are released before the interval and have remaining execution (carry-in jobs)
  Form a necessary un-schedulability test from IUB and necessary condition for deadline miss

## Slide 18: Global scheduling
Based on the previous test and assuming global EDF algorithm, the job of τk misses its deadline if the load in the interval is at least m(1−δk ) +δk
A constrained-deadline task set is schedulable under pre-emptive global EDF scheduling if for every task
For fixed task priority, this response time upper bound is

## Slide 19: Global scheduling
Pfair algorithm (Proportionate fairness algorithms)
Motivations
  All mentioned mutliprocessor scheduling have maximum utilization bound 50%
  Ideally, a utilisation bound of 100% is more interesting.
The algorithm is the only known optimal scheduling for periodic implicit deadline task
It is based on dynamic job priority
Timeline is divided into equal length slots
Tasks period and execution time is a multiple of the slot size
Each task receives amount of slots proportional to the task utilization
Disadvantages of Pfair
  Computational overheads are relatively high
  Too many preemptions (up to 1 per quantum per processor)

## Slide 20: Hybrid/semi-partitioned
What if some tasks are allocated to specific processor and other are scheduled globally?
Example:
  t1, t3 and t5 are assigned to P1
  t2 and t7 are assigned to P2
  t4 and t8 can be executed in P1 and P2
This kind of scheduling is called hybrid or semi-partitioned multiprocessor scheduling

## Slide 21: Hybrid/semi-partitioned
EKG approach
Assuming periodic task model and implicit deadline
Use bin packing algorithm to allocate tasks to processors
Tasks that can not fit into processors are splitted into up to k parts
Split tasks can be executed in up to k processors out of m

## Slide 22: Hybrid/semi-partitioned
If k=m
  Tasks are assigned using “next-fit” bin-packing
  Processors are filled up to 100%
  Example

## Slide 23: Hybrid/semi-partitioned
If m < k
  Tasks are categorized as heavy or light
  Heavy task has Ui > SEP=k(k+1), otherwise tasks are considered as light
  First, all heavy tasks are assigned to processors, one in each processor
  Light tasks are assigned to the processors using the remaining utilization
  The utilization bound is equal to m * SEP
Dispatching
  Partitioned tasks are scheduled using EDF
  Reservations are used in each processor to execute the split tasks and the priority of the reservation is always greater than the other tasks
  The reserves of τi on Pp and Pp+1 can never overlap.
Overhead
  For split tasks, each may cause up to k-migration every task period

## Slide 24: Cluster scheduling
Combining partition and global scheduling
Tasks are grouped into a set of clusters
Each cluster is allocated to a number of cores m less than or equal to the total number of cores n i.e., m ≤ n. Tasks within a cluster can be migrated between only the processors that are allocated for that cluster
P1
P2
P3
…
Tasks
Processors
P4

## Slide 25: Cluster scheduling
Physical clusters, allocated to m certain cores
Virtual clusters can be allocated to any m available cores (hierarchical scheduling, a scheduler to select clusters and inside each cluster there is a scheduler that selects the tasks to execute )

## Slide 26: Mutliprocessor synchronization
All presented algorithms do not support resource sharing
In multiprocessor, there are three general approaches
  Lock based
  Lock free
  Wait free
Lock based: each task locks a mutes before accessing a shared resource, and releases it when it finishes.
Resources can be classified as local resource and global resource
When a task is blocked trying to access a shared resource:
  It is suspended until the resource become available
  Continue executing in a busy wait

## Slide 27: Mutliprocessor synchronization
Partitioned scheduling, suspension
Problems:
  Remote blocking: tasks may be blocked by other tasks located in other processors (no direct relation between tasks)
  Multiple priority inversions due to suspensions (low priority tasks may execute while the higher priority tasks are suspended and accessing global resources)
Hp task
Lp task
Remote blocking
P 1
P 2
Critical
section

## Slide 28: Mutliprocessor synchronization
MPCP (multiprocessor priority ceiling protocol)
  Reduces and bounds the remote blocking
  applicable to partitioned systems using fixed priorities
  Global mutex Is used to protect global resources
  Priority ceiling=Max (All executing task priorities) +
      Max (priorities of tasks accessing the shared resource)
  A task accessing a global shared resource can be preempted by a awakened waiting task on a higher priority ceiling
  Each global resource has a priority queue
  No nested access to shared resources is allowed
  The blocking factor is made up of five different components

## Slide 29: Mutliprocessor synchronization
MPCP
Priority queue
Priority queue
Priority Queue
Shared
Resource
Pi
Pj

## Slide 30: Mutliprocessor synchronization
MSRP for partitioned scheduling
  Based on SRP protocol for single processor
  Can be used with FPS and EDF
  when a task is blocked on a global resource under MSRP, it busy waits and is not preemptable
  A FIFO queue is used to grant access to tasks waiting on a global resource when it is unlocked
Comparing MPCP and SRP
  MSRP removes two of the five contributions to the blocking factor
  MSRP Consumes processor time that could be used by other tasks
  MSRP is simpler to be implemented

## Slide 31: Mutliprocessor synchronization
Lock free approach
Tasks access resources concurrently
A task repeats the access to a shared resource whenever the input data is changes due to a concurrent access by another task
Lock-free approach increases the execution times of tasks
Typically, requires hardware support

## Slide 32: Mutliprocessor synchronization
Wait free
Multiple buffers are used
Does not impose blocking on the tasks accessing shared resources nor increasing the execution times of tasks
Requires more memory allocation (buffers)

## Slide 33: Other related issues
Parallel task model
Worst-case Execution Time (WCET) analysis
Network / bus scheduling
Memory architectures
Scheduling of uniform and heterogeneous processors
Operating Systems
Power consumption and dissipation
Scheduling tasks with soft real-time constraints
Many cores architecture
Virtualization